## Slide 1: Linear Clustering Process on Networks
Presenter: Beichen Wang
Thesis advisor: Prof. Piet Van Mieghem
Daily supervisor: Ivan Jokić
14/04/2023
MSc Thesis Mid-term Review
Notes: I’m going to introduce the current progress of my msc thesis and future plans as well. The topic is …

## Slide 2: Content
Linear Clustering Process
Other involved clustering algorithms
Benchmarks
Results
(Symmetric) Stochastic Block Model
LFR benchmark
SSBM & LFR
Real-world networks
Modularity-based
Local Dominance
LCP with known number of clusters
Random networks (ER, BA, WS)
Spectral method
Non-back tracking LCP
Notes: For today, I’m going to firstly briefly introduce the LCP since most of you have already known the story. This time I will elaborate a bit more about other algorithms we use to compare with the LCP. Furthermore, we measure all above algorithms on these two benchmarks and finally we will show the simulation results

## Slide 3: Network Clustering
Network clustering represents “organization of nodes in clusters, with many links joining nodes of the same cluster and comparatively few links joining nodes of different clusters” [1].
Widely accepted quality function for a given network partition is modularity index m.
A simple graph with three communities, from [1]
[1] Fortunato, S., 2010. Community detection in graphs. Physics reports, 486(3-5), pp.75-174.
Adjacency matrix
Number of links
Node i degree
Modularity index
Notes: Our task is called network clustering. As fortunato said, Network clustering is organization of nodes in clusters, with many links within clusters and few links between different clusters. Since clustering is non-supervised process, We need the help of quality function. Modularity is a widely used and accepted quality function. LCP is based on this.

## Slide 4: Linear Clustering Process (LCP) Node-level governing equation
Each node in the graph G is assigned a position on a line at discrete time .
LCP consists of two opposite and simultaneous forces that change nodal position in time
  Attraction: Adjacent nodes that share many common neighbours (i.e. triangles!) are mutually attracted.
  Repulsion: Two adjacent nodes are repulsed with a force proportional to the number of neighbours they do not share.
Attraction strength
Repulsive strength
Node i neighbours
Node i position
in time k
Time
Notes: The main idea of LCP is here. Firstly, each node in the graph is assigned a position on a line. This position is affected by two forces, attraction and repulsion. Adjacent nodes that share many common neighbours are mutually attracted because they are more likely to be in the same community. Meanwhile adjacent nodes sharing few neighbors are repulsed. We write down this process as this governing equation.

## Slide 5: Linear Clustering Process (LCP) Node-level governing equation
The attractive force between two adjacent nodes is always of higher strength than
the repulsive force, preserving the system's stability but negatively influencing the steady-state.
Although the repulsive force is a simplified version of the Newtonian repulsive force,
the LCP is proportional to the graph topology, which helps revealing the clusters.
Notes: This denotes the number of common neighbours. The attractive force is always higher than the repulsive force to make sure the system is stable. But this leads to a problem that steady state of this linear process will no longer be the result of clustering but all nodes in the same position. To avoid this, the process need a early stop.

## Slide 6: Linear Clustering Process (LCP) Network-level governing equation
adjacency matrix
node position vector
Degree matrix
identity matrix
Hadamard product
Node-level
Network-level
Notes: Here we write governing equation from node level to network level. Eigenvalue decomposition

## Slide 7: Cluster estimation based on the eigenvector y2
To estimate the clusters based on the eigenvector , we need to detect the borders of the clusters in the sorted vector .
We determine the borders of clusters by optimising recursively the modularity index .
Notes: Instead of using the largest eigenvalue, we use the second largest one. We calculate the component of y2 on each node and sort y2. Here we’ve already observed the partition. Relabel the network base on sorted y2. We determine the borders of clusters by optimising the modularity recursively. This is the whole idea of LCP.

## Slide 8: Existing clustering algorithms
Newman method (2006 PNAS, complexity )
Louvain method (2008 JSM, complexity for sparse networks)
Eigen gap method (2009 PRE, complexity )
Non-back tracking method (2013 PNAS, complexity )
Leiden method (2019 Nature Scientific Reports, for sparse networks)
Local dominance (2022 arXiv, complexity )
Notes: Here is all algorithms we involved now and their publish time and complexity.

## Slide 9: Existing clustering algorithms
Newman method (2006 PNAS, complexity )
Louvain method (2008 JSM, complexity for sparse networks)
Leiden method (2019 Nature Scientific Reports, for sparse networks)
Eigen gap method (2009 PRE, complexity )
Non-back tracking method (2013 PNAS, complexity )
Local dominance (2022 arXiv, complexity )
Modularity-based
Spectral method
Hierarchy method
Notes: Actually, these algorithms can be divided into these three categories …. For Newman and Louvain, their objective is to optimize the modularity like LCP did. Leiden is a improvement of Louvain which has higher quality of community partition. Eigen gap and NBT are spectral method. Different from the modularity-based method, these methods can only produce the number of clusters. LCP has a NBT version, which replace NBT matrix with W matrix and others remain the same. Local is a hierarchy method. They transformed the network into a tree according to the relationship between the degree of a node and its neighbors.

## Slide 10: Performance metrics
Estimated number of clusters c
Modularity m
Normalised Mutual Information (NMI)
Element-centric Similarity (ECS)
Notes: We now have four performance metrics. C,m. Both NMI and ECS are used to measure the similarity of two clustering results, or we say estimated partition and ground-truth. NMI is widely accepted metric. ECS is a relatively new metric. But after it was published in nature in 2019, there are more and more papers using it because they believe ECS is more fair than NMI.

## Slide 11: Performance metrics
Notes: Let’s take a look at the difference between ECS and NMI. Here are two scenarios. For a, NMI still work well because NMI between Left and middle partition is higher than between right and middle. But it's still counter-intuitive for me because NMI is equal to zero but node 7,8,9 should be correct. ECS=1/3, fair enough. For b, NMI is wrong here but ECS is still correct. Therefore, ECS is more fair and NMI somehow encourages the algorithm to cluster more communities instead of less

## Slide 12: Simulation Results
Stochastic Block Model (SBM)
LFR benchmark
Random graph models (ER, BA, WS)
Real-world networks

## Slide 13: Stochastic Block Model (SBM)
Two nodes are connected via a link with probability if they belong to the same cluster, otherwise the direct link exists with probability .
Communities emerge when the link density within clusters is larger than the inter-community link probability .
,
An example of SSBM network with
N = 1000 nodes and c = 5 clusters.
Notes: SBM is a random model. We use pin and pout to control the link density within clusters and inter-community links. Communities become visible when pin is larger and pout. Every cluster has same size.

## Slide 14: SBM benchmark results
Notes: X-axis is bin-bout, this vertical line show the threshold of SBM. After this line, bin is larger than bout so that clusters become visible. Spectral methods dominant number of clusters. LCP-NBT shows the same performance of NBT. LCP better than all other mod-based method. LCP always has highest mod. But LCP begin to have good NMI only after threshold because LCP found different partition from original. Better NMI means get closer to the green curve, original mod. LCP dominants ECS, and we can observe a huge improvement of LCP with known number of clusters. When the number of clusters is relatively small, here equals to 2, this improvement is significant.

## Slide 15: SBM benchmark results
Notes: Performance quite similar, the improvement shrink when the c increases. And this improvement only happen with difficult cases.

## Slide 16: SBM benchmark results
Notes: No improvement since c is perfect.

## Slide 17: SBM benchmark results
Notes: More difficult for these algorithms. Mod-based method seems have no idea of c. Spectral methods converge at the end. LCP still has highest mod but cannot dominant ECS anymore.

## Slide 18: LFR benchmark
The degree vector is sampled from a power-law distribution with exponent .
The community size vector is sampled from a power-law distribution with the exponent .
Each node shares ratio of links with nodes from other communities.
An example of the LFR network with
N = 500 nodes, c = 10 clusters and
parameters , and .
Notes: LFR benchmark is power-law network. Not only degree distribution conforms to power-law, but also community size.

## Slide 19: LFR benchmark results
Notes: X-axis is μ, ratio of links between clusters. NBT is best on c but NBT LCP failed this time. LCP is still better than other mod-based methods.

## Slide 20: LFR benchmark results
Notes: C=10 more difficult. LCP is best.

## Slide 21: Random network results
Erdős-Rényi
Barabási-Albert
Watts-Strogatz
Notes: These random networks have no clustering structure so we expect these algorithms to output c as close to 1 as possible. For ER and BA, NBT dominant and NBT LCP performs the same. LCP still better than other mod-bases. For WS, it’s a bit weird since spectral methods fail and Louvain and Leiden performs best and then LCP. Still, LCP has highest mod on these cases.

## Slide 22: Real-world networks
Political Blogs
Network | N | L
Karate Club | 34 | 78
Dolphins | 62 | 159
Polbooks | 105 | 441
Football | 115 | 613
Facebook | 347 | 2519
Polblogs | 1490 | 19090
Co-authorship | 1589 | 2742
Notes: We found some real-world networks and here is their number of nodes and links.

## Slide 23
Results for the real-world networks
Network | LCP |  | Louvain |  | Leiden |  | Newman |  | Local dominance |  | Non-back tracking | Non-back tracking LCP | Eigengap
 | c | m | c | m | c | m | c | m | c | m |  |  | 
Karate | 3 | 0.3922 | 4 | 0.3565 | 4 | 0.3729 | 5 | 0.3776 | 2 | 0.3123 | 2 | 1 | 2
Dolphins | 4 | 0.5057 | 4 | 0.4536 | 5 | 0.5105 | 6 | 0.4894 | 3 | 0.3620 | 2 | 2 | 2
Polbooks | 3 | 0.5160 | 4 | 0.4897 | 4 | 0.5026 | 8 | 0.4160 | 2 | 0.4451 | 3 | 2 | 2
Football | 7 | 0.5894 | 7 | 0.5442 | 7 | 0.5635 | 11 | 0.4623 | 6 | 0.3205 | 10 | 5 | 11
Facebook | 8 | 0.4089 | 16 | 0.3726 | 18 | 0.3792 | 23 | 0.3770 | 8 | 0.2067 | 8 | 4 | 2
Polblogs | 19 | 0.4224 | 7 | 0.3385 | 11 | 0.3117 | 4 | 0.3459 | 3 | 0.2799 | 8 | 1 | 2
Co-authorship | 40 | 0.9296 | 272 | 0.9423 | 270 | 0.9410 | 28 | 0.7393 | 277 | 0.9431 | 23 | 16 | 2
Notes: Since we don’t know their ground-truth communities, we can only use mod to evaluate the performance. LCP gives highest modularity 5 out of 7.

## Slide 24: Real-world networks with ground-truth communities
Network | N | L | C | Modularity
Email_eu | 1005 | 25571 | 42 | 0.2880
Cora | 2708 | 5429 | 7 | 0.6401
Citeseer | 3264 | 9072 | 6 | 0.5042
Citeseer
Notes: We think it’s not good enough to only use mod so here we found another 3 networks with ground-truth communities.

## Slide 25
Results for the real-world networks with ground-truth communities
Network | C | M | LCP |  |  |  | Louvain |  |  |  | Leiden |  |  | 
 |  |  | c | m | nmi | ecs | c | m | nmi | ecs | c | m | nmi | ecs
Email_eu | 42 | 0.2880 | 9 | 0.3860 | 0.5466 | 0.2513 | 12 | 0.3795 | 0.5530 | 0.2747 | 17 | 0.3745 | 0.6352 | 0.3711
Cora | 7 | 0.6401 | 25 | 0.7296 | 0.3138 | 0.2121 | 86 | 0.6775 | 0.3691 | 0.2808 | 85 | 0.7403 | 0.4201 | 0.2722
Citeseer | 6 | 0.5042 | 65 | 0.8027 | 0.1399 | 0.0737 | 394 | 0.7722 | 0.3095 | 0.1878 | 395 | 0.7367 | 0.3438 | 0.2064
Network | C | M | Newman |  |  |  | Local dominance |  |  |  | Non-back tracking | Non-back tracking LCP |  | Eigengap
 |  |  | c | m | nmi | ecs | c | m | nmi | ecs |  |  |  | 
Email_eu | 42 | 0.2880 | 14 | 0.3492 | 0.5668 | 0.3003 | 1 | 0.0000 | 0.0000 | 0.0669 | 17 | 1 |  | 5
Cora | 7 | 0.6401 | 68 | 0.7166 | 0.4146 | 0.1896 | 181 | 0.6728 | 0.4271 | 0.1648 | 40 | 39 |  | 2
Citeseer | 6 | 0.5042 | 311 | 0.8276 | 0.3307 | 0.0560 | 505 | 0.7691 | 0.3889 | 0.0619 | 17 | 16 |  | 3
Notes: Leiden performs best. LCP loses its advantage on these three networks. LCP still has high modularity but way higher than original since LCP found totally different clusters so that NMI and ECS is low.

## Slide 26: Conclusions
Among considered clustering algorithms, LCP is superior in modularity consistently;
In case when clusters are visible in a graph, LCP identifies partitions with the highest NMI measure
  In other cases, LCP provides lower NMI value, because it identifies different partition from the original one, but with higher modularity;
LCP dominants ECS metric even when clusters are not visible. And ECS reveals how real number of clusters as input benefit LCP partitions;
Non-back tracking LCP algorithm achieves as good results as the non-back tracking method except LFR benchmark, while providing a clear underlying process and reasoning.

## Slide 27: Appendix

## Slide 28: Time-dependence of the LCP
If all nodes share the same position, the LCP is in a trivial steady state. Thus, the all-one vector u is a trivial solution for the steady-state of LCP.
Instead, the hierarchical structure of the network
emerge in the time evolution of LCP!
A scaled and shifted nodal position vector tends to the eigenvector with an exponentially decreasing error in time k. Thus, we estimate the clusters based on .

## Slide 29: Modularity index m optimisation
Based on the sorted eigenvector , we define the permutation matrix R and transform the adjacency matrix A and the degree vector d.
Transformed relation defines the modularity index m as a sum of the elements of the matrix within brackets, corresponding to clusters.
Such definition allows for a simple recursive optimisation.

## Slide 30: Scaling the weights of inter-community links
Non-linearity in the forces can be introduced in the proposed linear clustering process iteratively by scaling the weights of inter-community links between iterations, that artificially decreases the strength of forces between the two nodes from different clusters.
we reduce the importance of links between nodes from different clusters, based on the partition from previous iteration.

## Slide 31: Newman method
To maximize the modularity m, Newman proposes to make recursive splits according to the leading eigenvector of the modularity matrix M. The modularity m can be rewritten as:
which y is composed of values 1 and −1, denoting cluster membership of each node, the modularity matrix
The vector y can be written as a linear combination of the orthogonal eigenvectors w1, w2, ... ,wN of the modularity matrix M, y= , with coefficients βj = yTwj. Therefore, maximizing the modularity m is equivalent to choosing the vector y with cluster memberships proportional to the eigenvectors corresponding to a few of the largest eigenvalues.

## Slide 32: Louvain method

## Slide 33: Leiden method

## Slide 34: Non-backing tracking method

## Slide 35: Eigengap method

## Slide 36: Local Dominance

## Slide 37: SBM benchmark results

## Slide 38: LFR benchmark results

## Slide 39: LFR benchmark results

## Slide 40: LFR benchmark results

## Slide 41: LFR benchmark results